## Slide 1: Computer Organization & Architecture
“Computer Organization and Embedded Systems”
Carl Hamacher, Zvonko Vranesic, Safwat Zaky, Naraig Manjikian

## Slide 2: Fundamentals
Instruction:
  Fetched from memory location pointed by program counter PC
  Put in the Instruction Register IR
  IR <- [[PC]]
  PC <- [PC] + 4

## Slide 3: Operations
Can be carried out by performing one or more of the following actions:
  Read contents of a memory location and load into a processor register
  Read data from one or more processor registers
  Perform arithmetic or logic operation and place result into a processor register
  Store data from a processor register into a memory location

## Slide 4: Main H/W Components of Processor
Register File
Instruction Address Generator
Processor Memory Interface
IR
Control Circuitry
PC
ALU

## Slide 5: Register File
Register ﬁle are storage locations:
  Organized to form processor’s general-purpose registers
  Registers comprise edge-triggered ﬂip-ﬂops
    Into which new data are loaded at the active edge of the clock

## Slide 6: Execution
During execution:
  Contents of specified registers are sent to arithmetic and logic unit (ALU)
  ALU performs the required computation
  Data are processed by combinational circuits and results placed into a register
  Results of computation are stored in a register in register ﬁle
  A clock signal is used to control timing of data transfers

## Slide 7: Instruction execution
LOAD instruction
Ex. Load R5, X(R7)
  Fetch the instruction from the memory
  Increment the program counter
  Decode instruction to determine operation to be performed
  Read register R7
  Add immediate value X to the contents of R7
  Use sum X + [R7] as effective address of source operand
    Read the contents of that location in the memory
  Load data received from memory into destination register, R5

## Slide 8: Multi-stage structure
Operations can often be broken down into several simpler steps
  Each step is performed by a subcircuit of the original circuit
  Subcircuits can be cascaded into a multistage structure
  If n stages are used, operation will be completed in n clock cycles
  Since subcircuits are smaller, they can complete operation in less time, and hence a shorter clock period can be used
Key advantage of the multi-stage structure is that it is suitable for pipelined operation
  Particularly useful for implementing processors that have a RISC-style instruction set

## Slide 9: Multi-stage structure
Assuming processor has ﬁve hardware stages, execution of each instruction is divided into ﬁve steps:
  Fetch instruction and increment the program counter
  Decode instruction and read source operands
  Compute
  Access memory for read/write
  Store result in register file

## Slide 10: Load instruction
LOAD R5, X(R7)
  Fetch instruction and increment the program counter
  Decode instruction and read contents of register R7
  Compute the effective address
  Read the memory source operand
  Load the operand into the destination register, R5

## Slide 11: Arithmetic/Logical instruction
Ex. Add R3, R4, R5
  Fetch the instruction and increment the program counter
  Decode instruction and read contents of source registers R4 and R5
  Compute the sum [R4] + [R5]
  Load the result into the destination register, R3

## Slide 12: Arithmetic/Logical instruction
It is advantageous to use same multistage processing hardware for as many instructions as possible
  Can be achieved if all instructions are made to be executed in the same number of steps
  To this end, Add instruction should be extended to ﬁve steps

## Slide 13: Arithmetic/Logical instruction
Add instruction would then be performed as follows:
  Fetch the instruction and increment the program counter
  Decode the instruction and read registers R4 and R5
  Compute the sum [R4] + [R5]
  No action
  Load the result into the destination register, R3

## Slide 14: Arithmetic/Logical instruction
Ex. Add R3, R4, #1000
  Fetch the instruction and increment the program counter
  Decode the instruction and read register R4
  Compute the sum [R4] + 1000
  No action
  Load the result into the destination register, R3